## Slide 1
1
School of Electronics Engineering (SENSE)
MDP (2026)
Self-Powered Gym-Locker Beacon via Human Wearable Thermoelectric Harvesting
Student Team:
Naasim Theyyambattil — 26BYB1051 Amruth Reddy Yamasani — 26BRS1148 Shreyas Jha — 26BRS1149 V. Monish Shri Hari — 26BVD1072 Mridula Muthukumaran — 26BEC1637
Guide:
JEIPRATHA P N
Programme / School:
B.Tech — AI Robotics (FEPT), SENSE, VIT Chennai
Review & Date:
Review-II · 14.10.2026 (Wednesday)
Guide's Signature with Date
Signature: _____________________
Date: _________________________
Approval is mandatory before the review. Guide signature and dated scanned approval must be inserted before final submission.

## Slide 2
2
Introduction
Problem statement
Wearable gym/locker beacons typically need a battery or regular charging. Replacing many small batteries adds maintenance and e-waste; a body-heat harvester could reduce that burden, but available thermal power is small and varies with the environment.
Project objective
• Design a wrist-worn proof of concept that harvests skin-to-ambient heat using a thermoelectric generator (TEG).
• Condition and store the low-voltage output with an LTC3108-based energy-harvesting stage and a supercapacitor.
• Test whether stored energy can support a short Bluetooth Low Energy (BLE) locator advertisement from an ultra-low-power controller.
Review-II scope
This is proposal-stage work: no circuit has been built and no measurements have been collected yet. Claims about 10–50 mV, sweat-assisted cooling and battery-free operation are hypotheses to validate, not results.

## Slide 3
3
Detailed Literature Review (1/3)
No. | Author(s) & Year | Title / Source | Method / Approach | Findings & Research Gap
[1] | Smith & Johnston (2021) | Skin-worn TEGs for body-heat harvesting | Experimental wearable setup measuring voltage, power and energy at the skin. | Shows that real worn-condition output must be measured. Gap: not designed around this project’s BLE burst budget.
[2] | Sun, Wang & Jiang (2022) | Challenges and strategies for human-body TEGs | Review of device physics, heat transfer, materials and wearable integration. | Small temperature differences and thermal interfaces limit output. Gap: no specific wrist-beacon implementation.
[3] | Zhu et al. (2022) | Wearable TEGs: devices to applications | Review of inorganic TEG materials, topology, fabrication and applications. | Thermal-gradient and geometry optimization are central. Gap: end-to-end stored-energy vs. radio-event validation.
[4] | Fan et al. (2022) | High-power-density wearable TEGs | Rigid, substrate-free generator with 48 p–n pairs; tests with/without airflow. | Reported 7.9 µW/cm² without airflow and 43.6 µW/cm² under walking-like airflow. Gap: specialized device, not a stock TEC1-12706 wrist assembly.
[5] | Tabaie & Omidvar (2023) | Body-heat TEGs for wearable electronics | Review of recent body-heat harvesting systems and limiting factors. | Skin contact, environmental conditions and low ΔT strongly affect performance. Gap: application-specific power management remains needed.
[6] | Liu, Riba & Moreno-Eguilaz (2023) | BLE sensor-node energy balance with TEG harvesting | Models and evaluates the energy balance of BLE wireless sensor nodes powered by TEGs. | Closest precedent for pairing BLE with TEGs: harvested energy must exceed node and radio energy. Gap: different node, source and duty cycle.
Body-heat harvesters are environment- and interface-dependent; compare outputs only when ΔT, airflow and load are stated.

## Slide 4
4
Detailed Literature Review (2/3)
No. | Author(s) & Year | Title / Source | Method / Approach | Findings & Research Gap
[7] | Fan et al. (2023) | High-performance stretchable TEG | Stretchable TEG tested on forehead at 15 °C ambient, with natural and forced airflow. | Reported 13.8 µW/cm² in still air and up to 71.8 µW/cm² at 2 m/s. Gap: conditions may not match a warm, humid gym or wrist.
[8] | Zhang et al. (2023) | Dynamic response of skin-waste-heat TEGs | Bioheat-transfer model including skin layers and skin–TEG thermal contact. | Predicted more than 10 min to steady state after thermal perturbation. Gap: transient wrist/sweat behavior needs measurement.
[9] | J. Liu et al. (2023) | Materials, structures and fabrication of wearable TEGs | Critical review of materials, device structures, fabrication and application studies. | Wearability, thermal transfer and electrical output must be co-designed. Gap: commercial module + practical storage + BLE integration.
[10] | Newby, Mirihanage & Fernando (2024) | Knitted 3D-spacer wearable TEG | Knitted 3D spacer structure with detachable p–n junctions for body-heat harvesting. | Explores flexible textile integration and replaceable junctions. Gap: no validation of a compact wrist beacon’s energy budget.
[11] | Xiao et al. (2024) | Organic thermoelectric materials for wearables | Review of organic thermoelectric materials and wearable-device integration. | Flexible materials can improve comfort; material conductivity and durability remain trade-offs. Gap: this project uses a candidate off-the-shelf module.
[12] | Zadan et al. (2024) | Stretchable TEGs for wearable health monitoring | Stretchable composite generators characterized during sitting, walking and running. | Demonstrates activity-dependent wearable harvesting. Gap: radio-event energy and supercapacitor recharge time are not the target metric.
Cross-study numbers are not directly comparable unless device area, airflow, temperature difference and electrical load match.

## Slide 5
5
Detailed Literature Review (3/3)
No. | Author(s) & Year | Title / Source | Method / Approach | Findings & Research Gap
[13] | Erturun (2024) | TEG-powered wearable sensor face mask | Prototype combines a commercial mask, TEG and heat sink for sensor power. | Shows a practical wearable geometry for body-heat harvesting. Gap: breathing/face thermal conditions differ from a wristband.
[14] | Proto et al. (2024) | Body-heat harvesting in real-life scenarios | Bendable miniature TEGs with a polyacrylic heat sink; evaluated in real use. | Reported reduced effectiveness when ambient temperature exceeds 30 °C. Gap: validate under local gym temperature/humidity and wrist airflow.
[15] | Kim et al. (2024) | TEG optimization by fill factor and leg geometry | Experimental and theoretical comparison of TEG fill factor and leg geometry. | Generator geometry/contact resistance affects output. Gap: characterize the actual chosen module and its load-matched output.
Literature synthesis and project-specific gaps
What the literature establishes
• Wearable TEG output depends on the temperature difference actually maintained across the generator—not just skin temperature. • Airflow, contact resistance, module geometry and ambient conditions can change output substantially. • BLE feasibility must be judged from stored energy and measured radio-event energy, not open-circuit voltage alone.
Research gap addressed by this MDP
A wrist-scale, low-cost prototype must jointly verify: (1) realistic TEG voltage and loaded power; (2) LTC3108 startup and reservoir charging; (3) capacitor energy available above the controller’s brownout limit; and (4) repeatable BLE advertising under a measured energy budget. No reviewed paper is claimed to validate this exact combination.

## Slide 6
6
Formulation of the Problem
Battery maintenance & replacement burden
Tiny, variable heat energy available
Energy conversion, storage & radio peaks
Need measurable energy-neutral bursts
Core feasibility condition
Energy harvested and stored between bursts must cover startup + controller wake + BLE advertisement + conversion/leakage losses.
Critical assumptions to test (not yet demonstrated)
1 A useful ΔT exists across the TEG during real wear.
2 The LTC3108 starts and charges the reservoir at measured input.
3 The stored energy supports a repeatable BLE packet without reset.
Design note: the proposal’s 10–50 mV is an estimate to verify under load; the LTC3108’s 20 mV minimum-input specification does not itself guarantee startup or sufficient harvested power.
Notes: Insert your architecture / block diagram here.

## Slide 7
7
System Design & Architecture
Heat source Skin ↔ ambient ΔT varies
TEG Candidate TEC1-12706*
Power stage LTC3108 + matched transformer
Reservoir 0.22–1.0 F supercapacitor
Controller ESP32-C3 (short wake)
Locator BLE advertise then power down
Wake / transmit cycle
Charge while radio remains inactive
Reservoir reaches validated threshold
Enable controller; send one short BLE ad
Return to off / deep-sleep state; repeat if energy allows
Instrumentation path (for validation)
Measure Tskin, Tambient and TEG-face temperatures; record VTEG (open-circuit and loaded), Vcap vs. time, charge/discharge current, wake/advertisement energy, advertising success and range.
* TEC1-12706 is a candidate module used in generator mode; suitability and loaded output are unverified. Consider benchmarking a dedicated TEG if output is inadequate.
Notes: Insert your architecture / block diagram here.

## Slide 8
8
Implementation Details — Planned Work
Status at Review-II
No hardware, CAD enclosure or firmware has been completed yet. The items below are the implementation plan, not completed modules.
Hardware workstream
• Characterize TEG open-circuit voltage and loaded power across controlled temperature differences.
• Validate LTC3108 board/transformer compatibility and reservoir charging before connecting the radio.
• Measure capacitor leakage, usable voltage window and startup/restart behavior.
Firmware workstream
• Use a controllable enable/power-gating path; avoid relying on development-board deep sleep as proof of microamp system current.
• Transmit one short BLE advertisement per qualified charge threshold; record resets and packet success.
Planned control logic
Charge → check power-good / reservoir threshold → advertise once → disable radio/controller → recharge. Thresholds and timing will be set only after measurements.
Illustrative control flow (not compiled firmware)
loop: keep_controller_off() wait_until(reservoir_ready) if voltage_is_safe(): enable_controller() advertise_BLE_once() log_event_energy_if_instrumented() disable_controller() return_to_charge_state()
Acceptance checks
• LTC3108 starts with the measured TEG source. • Reservoir charges above controller brownout. • One BLE event succeeds without an external battery.

## Slide 9
9
Results & Analysis (20%) — Current Evidence
No experimental results collected yet — prototype and measurements are still pending.
Baseline evidence register
Metric
Current status
How it will be measured
Why it matters
TEG voltage / ΔT
Not measured
Thermocouples + DMM; open and loaded tests
Confirms source voltage under real conditions
Loaded TEG power
Not measured
Sweep known loads; calculate P = V × I
Open-circuit voltage alone is insufficient
Supercapacitor charge
Not measured
Record Vcap versus time and current
Estimates available stored energy / recharge time
BLE event energy
Not measured
Measure current over boot + advertisement
Checks whether each burst is feasible
Repeatability / range
Not measured
Count successful ads, resets and reception distance
Checks practical locator usefulness
Presentation integrity: blank measurement cells are intentional; values will be added after the corresponding tests are completed.
Notes: Add your results here — graphs, tables, screenshots or outputs.

## Slide 10
10
Results & Analysis (contd.) — Feasibility Checks
Illustrative stored-energy calculation (not a measured result)
Eusable = ½ C (Vhigh² − Vlow²) For C = 0.22–1.0 F and 3.3 → 3.0 V: ideal energy ≈ 0.208–0.945 J
Important limitation This is an ideal capacitor calculation only. ESR, leakage, converter losses, board quiescent current and voltage brownout reduce the energy actually usable by the radio.
Planned go / no-go gates
1 Source
Loaded TEG power is measurably above instrument noise under the intended wrist conditions.
2 Harvesting
LTC3108 starts repeatably and charges the reservoir within the available wear interval.
3 Radio
Stored energy covers boot + BLE advertisement with margin, without a brownout reset.
4 Sustainability
Repeat cycles achieve a practical locator interval without external electrical input.
If the measured source cannot pass Gate 1–2, revise the TEG/thermal design before attempting to claim self-powered BLE operation.
Notes: Add your results here — graphs, tables, screenshots or outputs.

## Slide 11
11
Challenges & Remaining Work
Main technical risks and response
• Low / variable thermal gradient: log skin, ambient and both TEG-face temperatures; compare still-air and moving-air conditions.
• Unverified TEC1-12706 suitability: measure loaded power first and benchmark a dedicated TEG if the commercial Peltier module underperforms.
• LTC3108 startup is not guaranteed by a nominal input-voltage specification alone: confirm the actual transformer, source impedance and loaded input.
• BLE peak demand and development-board overhead may exceed the available energy: instrument full-board current or use a low-leakage, power-gated implementation.
• Sweat, humidity, comfort and metal edges require careful enclosure design; the cooling plate benefit must be demonstrated, not assumed.
Remaining work / timeline to Review-III
• Week 1 — finalize literature and procurement; create safe benchtop thermal fixture.
• Week 2 — characterize TEG voltage/power vs. temperature difference and load.
• Week 3 — verify LTC3108 startup, capacitor charging, leakage and usable-energy window.
• Week 4 — implement a single BLE burst and measure event energy; add voltage-threshold control.
• Week 5 — integrate wristband/CAD enclosure, repeat controlled trials, report limitations and measured results.

## Slide 12
12
References (1/3)
[1] R. I. Smith and M. L. Johnston, “Analysis of Skin-Worn Thermoelectric Generators for Body Heat Energy Harvesting to Power Wearable Devices,” in Proc. 43rd Annu. Int. Conf. IEEE Eng. Med. Biol. Soc. (EMBC), 2021, pp. 7158–7161, doi: 10.1109/EMBC46164.2021.9629473.
[2] T. Sun, L. Wang, and W. Jiang, “Pushing thermoelectric generators toward energy harvesting from the human body: Challenges and strategies,” Materials Today, vol. 57, pp. 121–145, Jul.–Aug. 2022, doi: 10.1016/j.mattod.2022.06.001.
[3] S. Zhu et al., “Review on Wearable Thermoelectric Generators: From Devices to Applications,” Energies, vol. 15, no. 9, Art. no. 3375, 2022, doi: 10.3390/en15093375.
[4] W. Fan et al., “High-Power-Density Wearable Thermoelectric Generators for Human Body Heat Harvesting,” ACS Applied Materials & Interfaces, vol. 14, no. 18, pp. 21224–21231, 2022, doi: 10.1021/acsami.2c03431.
[5] Z. Tabaie and A. Omidvar, “Human body heat-driven thermoelectric generators as a sustainable power supply for wearable electronic devices: Recent advances, challenges, and future perspectives,” Heliyon, vol. 9, no. 4, Art. no. e14707, 2023, doi: 10.1016/j.heliyon.2023.e14707.
[6] Y. Liu, J.-R. Riba, and M. Moreno-Eguilaz, “Energy Balance of Wireless Sensor Nodes Based on Bluetooth Low Energy and Thermoelectric Energy Harvesting,” Sensors, vol. 23, no. 3, Art. no. 1480, 2023, doi: 10.3390/s23031480.
Every listed reference is cited in the literature review or technical-design slides.

## Slide 13
13
References (2/3)
[7] W. Fan et al., “High-Performance Stretchable Thermoelectric Generator for Self-Powered Wearable Electronics,” Advanced Science, vol. 10, no. 12, Art. no. 2206397, 2023, doi: 10.1002/advs.202206397.
[8] A. Zhang, D. Pang, B. Wang, and J. Wang, “Dynamic responses of wearable thermoelectric generators used for skin waste heat harvesting,” Energy, vol. 262, Part B, Art. no. 125621, 2023, doi: 10.1016/j.energy.2022.125621.
[9] J. Liu et al., “Wearable Thermoelectric Generators: Materials, Structures, Fabrications, and Applications,” physica status solidi (RRL) – Rapid Research Letters, 2023, doi: 10.1002/pssr.202200502.
[10] S. Newby, W. Mirihanage, and A. Fernando, “Wearable, Knitted 3D Spacer Thermoelectric Generator with Detachable p-n Junctions for Body Heat Energy Harvesting,” Sensors, vol. 24, no. 16, Art. no. 5140, 2024, doi: 10.3390/s24165140.
[11] R. Xiao et al., “Organic Thermoelectric Materials for Wearable Electronic Devices,” Sensors, vol. 24, no. 14, Art. no. 4600, 2024, doi: 10.3390/s24144600.
[12] A. Zadan et al., “Stretchable Thermoelectric Generators for Self-Powered Wearable Health Monitoring,” Advanced Functional Materials, vol. 34, no. 39, Art. no. 2404861, 2024, doi: 10.1002/adfm.202404861.
Every listed reference is cited in the literature review or technical-design slides.

## Slide 14
14
References (3/3)
[13] U. Erturun, “Energy harvesting face mask using a thermoelectric generator for powering wearable health monitoring sensors,” Electronics Letters, 2024, doi: 10.1049/ell2.13241.
[14] A. Proto et al., “Wearable device for body heat energy harvesting in real-life scenarios,” Sensors and Actuators A: Physical, vol. 379, Art. no. 115999, 2024, doi: 10.1016/j.sna.2024.115999.
[15] J. H. Kim et al., “Experimental and Theoretical Optimization of Wearable Thermoelectric Generators Based on Fill Factor and Leg Geometry,” ACS Applied Energy Materials, vol. 7, no. 20, pp. 9315–9326, 2024, doi: 10.1021/acsaem.4c01794.
[16] Analog Devices, “LTC3108: Ultralow Voltage Step-Up Converter and Power Manager,” product information and datasheet, https://www.analog.com/en/products/LTC3108.html (accessed Oct. 12, 2026).
[17] Espressif Systems, “ESP32-C3 Series Datasheet,” v2.4, https://documentation.espressif.com/esp32-c3_datasheet_en.html (accessed Oct. 12, 2026).
Paper references [1]–[15] plus manufacturer datasheets [16]–[17].

## Slide 15
15
Thank You
MDP (2026) · SENSE · VIT Chennai Self-Powered Gym-Locker Beacon via Thermoelectric Harvesting